## Slide 1
Speaker Recognition System
EEC201 FINAL PROJECT
OhCaptainMyCaptain
2025-03-19

## Slide 2
CONTENTS
Slide 1: Title
Slide 2: Overview
Slide 3: Implementation Highlights
Slide 4: Key Functions & Scripts
Slide 5: Test & Results (Part 1)
Slide 6: Test & Results (Part 2)
Slide 7: Observations
Slide 8: Conclusions
Slide 9: References & Acknowledgments

## Slide 3
01
Slide 1: Title

## Slide 4
Slide 1: Title
Team: OhCaptainMyCaptain
Members: Zherong Yu & Haoyang Li
LI’S PART
YU’S PART

## Slide 5
02
Slide 2: Overview

## Slide 6
Slide 2: Overview
This diagram shows how input speech is processed to extract features (e.g., MFCC), then compared against multiple speaker reference models. Each model computes a similarity measure, and the maximum (best match) determines the speaker ID. Thus, classification is done by picking the most similar speaker model based on extracted features.

## Slide 7
Performance:
Training accuracy up to 100%
Testing accuracy ~83%–97%

## Slide 8
03
Slide 3: Implementation Highlights

## Slide 9
Slide 3: Implementation Highlights
1. MFCC Extraction
- Frame, window, FFT, Mel filter bank, log + DCT
2. LBG VQ Codebooks
- Clusters MFCC vectors for each speaker
- Codebook = speaker’s centroid set
3. Notch Filter (Robustness Test)
Applies a second‐order notch filter to each test signal at given center frequency (e.g., 1000 Hz).Observes accuracy drop under this distortion, measuring system robustness.

## Slide 10
04
Slide 4: Key Functions & Scripts

## Slide 11
Slide 4: Key Functions & Scripts
melfb.m:
Purpose: Builds a Mel-spaced triangular filter bank.
How It Runs:
Takes number of filters p, FFT size n, and sampling rate fs.
Constructs a sparse matrix m of size (p x (n/2 +1)), where each row is one mel-scale triangular filter.
Why: This helps wrap the linear frequency axis into a mel scale, reflecting human auditory perception. It is used inside the MFCC extraction step to transform each STFT power spectrum into mel-frequency bins.

## Slide 12
Slide 4: Key Functions & Scripts
computeMFCC_all.m:
Purpose: Converts raw audio frames into Mel-Frequency Cepstral Coefficients (MFCC).
Core Steps:
Pre-emphasis: slightly boost high frequencies by y(t) = x(t) - 0.95 * x(t-1).
STFT: short-time Fourier transform, get power spectrogram.
Mel Filter Bank (melfb): compress frequency axis.
Log + DCT: produce the final MFCC frames.
How It Connects: This function is central to extracting speaker-relevant features from each audio file before classification.

## Slide 13
Slide 4: Key Functions & Scripts
runLBG.m:
Purpose: Creates a codebook (vector quantization) from a set of MFCC vectors.
What It Does:
Starts with a centroid (the mean of all MFCC vectors).
Splits each centroid iteratively, updates them by nearest-neighbor assignments, until reaching codebookSize codewords.
Why: We represent each word or speaker by a small set of codeword centroids. Classification then checks which codebook yields the smallest distortion to a test MFCC sample.

## Slide 14
05
Slide 5: Test & Results (Part 1)

## Slide 15
Slide 5: Test & Results (Part 1)
Test 1–4:
Test 1: Our human performance recognition rate is 72.7%.
Test 2: After the normalization of the 11 raw data from "train" folder, we plot the signal in time domain.
Use STFT to generate periodogram.

## Slide 16
Slide 5: Test & Results (Part 1)
Test 1–4:
Test 3: Plot the mel-spaced filter bank responses. Plot the spectrum of a speech after the melfrequency wrapping step.

## Slide 17
Slide 5: Test & Results (Part 1)
Test 1–4:
Test 4: Combining all steps into an MFCC extraction function.

## Slide 18
Test 5–6
Test 5: Visualizing MFCC 2D scatter for different speakers.

## Slide 19
Test 5–6
Test 6: Generating LBG codewords and plotting them over the MFCC scatter.

## Slide 20
06
Slide 6: Test & Results (Part 2)

## Slide 21
Slide 6: Test & Results (Part 2)
Test 7: ~87.5% test accuracy with standard clean data
Test 8: Applied notch filters – accuracy drops but remains viable
Test 9: Adding more speakers reduces accuracy to ~83.33%
Test 10a–10b

## Slide 22
Test 10a–10b
Multi-word tasks (e.g., “zero” & “twelve,” “five” & “eleven”)
Individual word recognition up to 95–100%, combined tasks ~80–95%

## Slide 23
Test 10a–Q2
Question 2: If we train a whole system that tries to identify
a) which speaker
b) whether the speech is "zero" or "twelve", how accurate is
In Test 10a Q2, we group all speakers together with the words “zero” or “twelve” into multiple classes, with each class representing a (speaker, word) pair. We then apply LBG clustering to the MFCC vectors from the training set to generate a codebook for each class. During testing, for an unknown audio sample, we select the codebook yielding the lowest distortion; this simultaneously identifies the speaker and the spoken word.

## Slide 24
07
Slide 7: Observations

## Slide 25
Slide 7: Observations
1. High Training Accuracy: 100% indicates potential overfitting but acceptable for small sets
2. Testing: 83–97% range, influenced by noise or added speakers
3. Noise Resilience: Performance degrades with notch filters but remains functional
4. Multi-word: Slight accuracy drop when classifying both speaker & word

## Slide 26
08
Slide 8: Conclusions

## Slide 27
Slide 8: Conclusions
MFCC + VQ is a straightforward, effective approach for small-scale speaker recognition
Scalability: More speakers/words need more data or advanced methods
Noise & Distortions: Additional preprocessing or robust features could help
Future Work: Explore deep learning (x-vectors) or data augmentatio

## Slide 28
09
Slide 9: Acknowledgments

## Slide 29
Repository: 201FinalProject on GitHub
Scripts: melfb.m, computeMFCC_all.m, runLBG.m
Data: Contributed by 2024/2025 students & instructors
Thank You!

## Slide 30
THE END
THANKS